## Slide 1
C14 + E11 + E12 · MODULE HOURS: 9 · FACULTY: DR. PALLAV SAHAY
Digital Logic Design
Module–1: Digital Logic Design Fundamentals
TEAM MEMBERS
25BCE10255
Naman
25BCE10310
Monil Gautam
25BCE10315
Maan
25BCE10383
Ansh Saikhedkar
25BCE10417
Kanav Luthra
25BCE10425
Madhav Singh Chauhan
25BCE10430
Krishna

## Slide 2
01 — NUMBER SYSTEMS
02 / 16
POSITIONAL NOTATION
Number Systems & Positional Notation
What is a number system?
A number system represents numbers using a fixed set of symbols (digits) and a base (radix). The value of a digit depends on its position.
General positional form
Any number N in base r can be written as:
N = Σ ( dᵢ × rⁱ )
from i = 0 to n−1 (integer part)
dᵢ = digit at position i
r = base (radix)
i = power / weight of that position
Worked example
(1011)₂
= 1×2³ + 0×2² + 1×2¹ + 1×2⁰
= 1×8 + 0×4 + 1×2 + 1×1
= 8 + 0 + 2 + 1
= 11₁₀
Each position has a weight that is a successive power of the base. The rightmost digit is always the least significant (r⁰).

## Slide 3
01 — NUMBER SYSTEMS
03 / 16
COMMON BASES
Binary, Octal, Decimal & Hexadecimal
System | Base | Valid Digits | Common Use
Binary | 2 | 0, 1 | Digital circuits, memory
Octal | 8 | 0 – 7 | Compact binary grouping
Decimal | 10 | 0 – 9 | Everyday counting
Hexadecimal | 16 | 0 – 9, A – F | Addresses, machine code
Why different bases matter
Binary is the native language of digital systems — every logic gate works with 0 and 1.
Octal & Hex give a compact way to write long binary strings (3 bits → 1 octal digit, 4 bits → 1 hex digit).
Decimal is what humans use; conversions between decimal and binary/hex are daily tasks in DLD.

## Slide 4
02 — BASE CONVERSIONS
04 / 16
BINARY ↔ DECIMAL / OCT / HEX
Number Base Conversions
Binary → Decimal
Expand each bit by its power of 2 and sum.
Example: (1101)₂
= 1·2³ + 1·2² + 0·2¹ + 1·2⁰
= 8 + 4 + 0 + 1
= 13₁₀
Decimal → Binary
Repeated division by 2.
Remainders read bottom → top.
Example: 13₁₀
13 ÷ 2 = 6 r 1
6 ÷ 2 = 3 r 0
3 ÷ 2 = 1 r 1
1 ÷ 2 = 0 r 1
→ (1101)₂
Binary ↔ Oct / Hex
Group bits:
3 bits → 1 octal digit
4 bits → 1 hex digit
Example: (101101)₂
Octal: 101 101 → 55₈
Hex: 0010 1101 → 2D₁₆
Pad with leading zeros if the bit length is not a multiple of 3 or 4.

## Slide 5
02 — BASE CONVERSIONS
05 / 16
DECIMAL ↔ OCT / HEX
Decimal, Octal & Hexadecimal Conversions
Decimal → Octal / Hex
Same idea as decimal→binary: repeated division by the target base. Remainders read from bottom to top.
Example: 156₁₀ → Hex
156 ÷ 16 = 9 remainder 12 (C)
9 ÷ 16 = 0 remainder 9
→ (9C)₁₆
For fractional parts: multiply the fraction by the target base and collect integer parts until the required precision.
Octal / Hex → Decimal
Expand by powers of the base.
Example: (2F)₁₆
= 2×16¹ + 15×16⁰
= 32 + 15 = 47₁₀
Octal ↔ Hex (via binary)
Convert each digit to its 3-bit (oct) or 4-bit (hex) binary group, then regroup. This is the fastest method in exams.

## Slide 6
03 — SIGNED NUMBERS
06 / 16
UNSIGNED VS SIGNED
Unsigned & Signed Binary Numbers
Unsigned Binary
All bits represent magnitude. There is no sign bit.
Range for n bits:
0 to 2ⁿ − 1
Example (8 bits): 0 … 255
Signed Binary
One bit is reserved for the sign.
MSB = Most Significant Bit = sign bit.
0 → positive
1 → negative
Three common schemes exist.
Three signed representations we study
1. Sign-magnitude 2. 1’s complement 3. 2’s complement
They differ in how the negative magnitude is encoded and in the range of values they can represent.

## Slide 7
03 — SIGNED NUMBERS
07 / 16
REPRESENTATIONS & RANGES
Signed Number Representations
Representing +5 and −5 in 8 bits
Form | +5 | −5
Sign-magnitude | 0000 0101 | 1000 0101
1’s complement | 0000 0101 | 1111 1010
2’s complement | 0000 0101 | 1111 1011
How −5 is obtained
Sign-mag: keep magnitude, set MSB = 1
1’s comp: invert every bit of +5
2’s comp: 1’s complement + 1
Ranges (n bits)
Sign-mag & 1’s:
−(2ⁿ⁻¹ − 1) … +(2ⁿ⁻¹ − 1)
(two zeros: +0 and −0)
2’s complement:
−2ⁿ⁻¹ … +(2ⁿ⁻¹ − 1)
(preferred in modern systems)

## Slide 8
04 — BOOLEAN ALGEBRA
08 / 16
FUNDAMENTALS
Boolean Algebra Fundamentals
Boolean algebra deals with variables that take only two values: 0 and 1. It is the mathematical foundation of digital logic.
AND ·
A · B or AB
1 only when both inputs are 1
Truth table
A B | F
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1
OR +
A + B
1 when at least one input is 1
Truth table
A B | F
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 1
NOT ¯
A̅ or A'
Inverts the value
Truth table
A | F
0 | 1
1 | 0

## Slide 9
04 — BOOLEAN ALGEBRA
09 / 16
BASIC LAWS
Basic Boolean Laws
Identity
A + 0 = A
A · 1 = A
0 does nothing to OR; 1 does nothing to AND
Null / Domination
A + 1 = 1
A · 0 = 0
1 forces OR to 1; 0 forces AND to 0
Idempotent
A + A = A
A · A = A
Repeating a variable has no effect
Complement
A + A̅ = 1
A · A̅ = 0
A variable and its complement cover all cases
Involution
(A̅)̅ = A
Double negation restores the original

## Slide 10
05 — BOOLEAN THEOREMS
10 / 16
COMMUTATIVE TO ABSORPTION
Boolean Algebra Theorems
Commutative
A + B = B + A
AB = BA
Order of operands does not matter
Associative
A+(B+C)=(A+B)+C
A(BC)=(AB)C
Grouping does not matter
Distributive
A(B+C)=AB+AC
A+BC=(A+B)(A+C)
AND distributes over OR and vice-versa
Absorption
A + AB = A
A(A+B) = A
A term already covered by a simpler term can be dropped

## Slide 11
05 — BOOLEAN THEOREMS
11 / 16
DE MORGAN & SIMPLIFICATION
De Morgan’s Theorems & Simplification
Theorem 1
(A + B)̅ = A̅ · B̅
Complement of OR → AND of complements
Theorem 2
(A · B)̅ = A̅ + B̅
Complement of AND → OR of complements
Simplification example
F = (A + B)̅ + AB
= A̅B̅ + AB (De Morgan)
= A̅B̅ + AB (already simple; no further absorption)
Common mistakes
• Forgetting to complement every variable
• Not swapping OR ↔ AND
• Treating Boolean · as arithmetic multiplication

## Slide 12
06 — BOOLEAN FUNCTIONS
12 / 16
EXPRESSIONS, SOP, POS
Boolean Functions & Expressions
Boolean function
A mapping from binary inputs to a binary output
Literal
A variable or its complement (A or A̅)
Product term
AND of literals (e.g. AB̅C)
Sum term
OR of literals (e.g. A + B̅ + C)
Minterm
Product term containing every variable exactly once
Maxterm
Sum term containing every variable exactly once
SOP (Sum of Products): F = A̅B + AB̅ + AB
POS (Product of Sums): F = (A + B)(A̅ + C)
Truth table → list of minterms (where F=1) or maxterms (where F=0) → Boolean expression.

## Slide 13
06 — BOOLEAN FUNCTIONS
13 / 16
CANONICAL FORMS
Canonical & Standard Forms
Canonical form — every term contains all variables exactly once.
Standard form — terms may omit some variables (still SOP or POS).
From truth table to Canonical SOP
A B C | F
0 0 0 | 0
0 0 1 | 1 → m₁
0 1 0 | 0
0 1 1 | 1 → m₃
1 0 0 | 0
1 0 1 | 1 → m₅
1 1 0 | 0
1 1 1 | 1 → m₇
F(A,B,C) = Σm(1,3,5,7)
Canonical POS (maxterms)
Rows where F = 0 become maxterms.
F(A,B,C) = ΠM(0,2,4,6)
Minterm mᵢ corresponds to the binary value of the row index.
Maxterm Mᵢ is the complement of that product term.

## Slide 14
07 — COMPLEMENTS
14 / 16
r’s & (r−1)’s
r’s Complement & (r−1)’s Complement
For a number in base r:
(r−1)’s complement → subtract each digit from (r−1)
r’s complement → (r−1)’s complement + 1
Decimal (r = 10)
9’s complement of 573:
999 − 573 = 426
10’s complement:
426 + 1 = 427
9’s = (r−1)’s
10’s = r’s
Binary (r = 2)
Original: 1011 0010
1’s complement:
0100 1101
(flip every bit)
2’s complement:
0100 1110
(1’s + 1)

## Slide 15
07 — COMPLEMENTS
15 / 16
SUBTRACTION
Binary Subtraction Using 1’s & 2’s Complement
1’s Complement Method
Example: 1011 − 0101
1. 1’s of subtrahend: 1010
2. Add: 1011
+ 1010
-------
1 0101
3. End-around carry → add 1 to LSB
0101 + 1 = 0110
Result = 0110 (positive)
If no end-around carry → result is negative; take 1’s complement and attach a minus sign.
2’s Complement Method
Example: 1011 − 0101
1. 2’s of subtrahend: 1011
2. Add: 1011
+ 1011
-------
1 0110
3. Discard final carry
Result = 0110 (positive)
If no final carry → result is negative and already in 2’s-complement form.
Exam tip: 2’s complement needs no end-around carry — that is why hardware prefers it.

## Slide 16
Thank you
Digital Logic Design · Module–1
Questions?